## Slide 1: Analytical and Machine Learning based Frameworks for Synthesis of Planar, Spherical and Spatial Mechanisms
By
Shashank Sharma

## Slide 2: Outline
Background and Motivation
Spatial Alt-Burmester Synthesis
Unified Motion Synthesis
Planar Alt-Burmester Synthesis
Planar Path Synthesis
Unified Simulation
Summary

## Slide 3: Background and Motivation

## Slide 4: What are Mechanisms?
A mechanism is a network of rigid links and joints with one link fixed.
Planar mechanism
Spherical mechanism
Spatial Platform

## Slide 5: Mechanism Design
Mechanism design involves finding a mechanism which carries out a user specified task.
The process involves selection of joint types and link dimensions.
Example – Eight-bar Theo-Jansen linkage enables robotic walking.

## Slide 6: Mechanism Design
Motion Synthesis
Path Synthesis
Function Synthesis
Design problems have been conventionally posed as Motion, Path or Function Synthesis problem.

## Slide 7: Problem Statement
Practical problems can include multiple constraints. Algorithms don’t exist for these scenarios.
Most of the research is focused on synthesis of Planar mechanisms.
Unify Path and Motion Synthesis as the Alt-Burmester Synthesis.
Unify Synthesis of Planar, Spherical and Spatial mechanisms.
Poses+ Path points
+ Input-output link relationship
Additional constraints:
Fixed pivot location,
Moving pivot location,
Link lengths, etc.
Planar + Spherical
+ Spatial Mechanisms
Motion + Path
Synthesis
Design Constraints
Solver
Solution mechanism
Mechanism Synthesis Approach

## Slide 8: Dissertation Contributions
Alt-Burmester Synthesis
- ML approach for spatial mechanisms
- Analytical approach for planar mechanisms
Motion Synthesis
- Analytical approach for unified synthesis of planar, spherical, and spatial mechanisms
Path Synthesis
- ML approach for spatial mechanisms
- Analytical approach for planar mechanisms
Kinematic Analysis
- Numerical approach to simulate planar, spherical and spatial mechanisms

## Slide 9: Conference Publications
Sharma, Shashank, and Purwar, Anurag. “Path Synthesis of Defect-free Spatial 5-SS Mechanisms using Machine Learning”, Proceedings of the ASME 2020 International Design Engineering Technical Conferences and Computers and Information in Engineering Conference, IDETC2020-22731.
Sharma, Shashank, and Purwar, Anurag. “Unified Motion Synthesis of Spatial Seven-bar Platform Mechanisms and Planar Four-bar Mechanisms”, Proceedings of the ASME 2020 International Design Engineering Technical Conferences and Computers and Information in Engineering Conference, IDETC2020-22718.
Sharma, Shashank, and Purwar, Anurag. “Using a Point-Line-Plane Representation for Unified Simulation of Planar and Spherical Mechanisms.” Proceedings of the ASME 2019 International Design Engineering Technical Conferences and Computers and Information in Engineering Conference. Volume5A: 43rd Mechanisms and Robotics Conference. Anaheim, California, USA. August 18–21, 2019. V05AT07A030. ASME. doi: 10.1115/DETC2019-98194
Sharma, Shashank, Purwar, Anurag, and Ge, Q. Jeffrey. “A Motion Synthesis Approach to Solving Alt-Burmester Problems by Exploiting Fourier Descriptor Relationship Between Path and Orientation Data.” Proceedings of the ASME 2018 International Design Engineering Technical Conferences and Computers and Information in Engineering Conference. Volume 5B: 42nd Mechanisms and Robotics Conference. Quebec City, Quebec, Canada. August 26–29,2018. V05BT07A077. ASME. doi: 10.1115/DETC2018-85567
Sharma, Shashank, Purwar, Anurag, and Ge, Q. Jeffrey. “Optimal Non-Uniform Parametrization for Fourier Descriptor Based Path Synthesis of Four Bar Mechanisms.” Proceedings of the ASME 2018 International Design Engineering Technical Conferences and Computers and Information in Engineering Conference. Volume 5A: 42nd Mechanisms and Robotics Conference. Quebec City, Quebec, Canada. August 26–29, 2018. V05AT07A033. ASME. doi: 10.1115/DETC2018-85568

## Slide 10: Journal Publications
Sharma S., Purwar A., 2020, “A Machine Learning Approach to Solving the Alt-Burmester Problem for Defect-free Spatial Mechanism Synthesis”, ASME. J. Comput. Inf. Sci. Eng., manuscript under preparation
Sharma S., Purwar A., 2020, “Unified Design of Spatial, Spherical and Planar Mechanisms for the Motion Synthesis Problem”, ASME. J. Mechanisms Robotics. JMR-20-1314, Under Review
Sharma, S., and Purwar, A. (May 26, 2020). “Using a Point-Line-Plane Representation for Unified Simulation of Planar and Spherical Mechanisms.” ASME. J. Comput. Inf. Sci. Eng. December 2020; 20(6): 061002. doi:10.1115/1.4046817
Sharma, S., Purwar, A., and Jeffrey Ge, Q. (December 17, 2018). “A Motion Synthesis Approach to Solving Alt-Burmester Problem by Exploiting Fourier Descriptor Relationship Between Path and Orientation Data.” ASME. J. Mechanisms Robotics. February 2019; 11(1): 011016. doi: 10.1115/1.4042054
Sharma, S., Purwar, A., and Jeffrey Ge, Q. (October 18, 2018). “An Optimal Parametrization Scheme for Path Generation Using Fourier Descriptors for Four-Bar Mechanism Synthesis.” ASME. J. Comput. Inf. Sci. Eng. March 2019; 19(1): 014501. doi: 10.1115/1.4041566

## Slide 11: Spatial Alt-Burmester Synthesis
A Machine Learning Approach to Solving the Alt-Burmester Problem for Defect-free Spatial Mechanism Synthesis

## Slide 12: Spatial Alt-Burmester Problem
Motion Synthesis
Alt-Burmester Synthesis
Path Synthesis

## Slide 13: 5-SS Mechanism
A 5-SS platform linkage consists of a rigid floating body supported by five legs, each with a spherical joint on both ends.
It is a one degree-of-freedom mechanism.
Spatial 5-SS Mechanism

## Slide 14: Defect-Free Mechanism Synthesis Problem
Spatial 5-SS mechanism coupler paths tend to have multiple branches and circuits.
Solution concepts need to satisfy input path requirements without defects for it to be useful.
Coupler paths of sample 5SS mechanism
Branch Defects
Circuit Defects

## Slide 15: Machine Learning based Algorithm

## Slide 16: Data Generation using a Kinematic Solver
Iterative solver based on Newton-Raphson method.
Eighteen constraint equations for RR links.
Fifteen MP coordinates and three C coordinates.
A data set of 10,000 defect-free coupler motions is generated.
Each motion consist of 25 path points and orientations
Constraint for an SS dyad
Newton Raphson Iteration
and Jacobian Matrix

## Slide 17: Data Preprocessing
Cleanup
Normalization (time, location, orientation, scale)
Balancing
Augmentation
Masking
10,000 Raw Motion Data
417,760 Masked Motion Data

## Slide 18: Preprocessing: Cleanup
Solver jumps from one branch to another during simulation.
Motions filtered based on C1 discontinuity in path and orientation.

## Slide 19: Preprocessing: Normalizing Time
Arc-length parametrization-based time independent representation.

## Slide 20: Preprocessing: Normalizing Location, Orientation, Scale & Orientation
Create a representation invariant to rigid transformations.
Mean is translated to origin.
Principal axes are rotated to align with XYZ axes.
Curve scaled to unit length.
Moving frame is aligned with ground frame at the start of motion.

## Slide 21: Preprocessing: Data Balancing & Augmentation
Balancing: Minimize bias in the learned model by under sampling common paths.
Similarity score based on path curvature, path torsion and orientations.
Mirroring: Add mirrored curves for the model to learn mirror invariance.
Some common coupler motions
Notes: Want the model to learn diverse paths.

## Slide 22: Preprocessing: Data Masking
To learn the underlying relationship between path-points and orientations, some orientations are masked.
Gaussian noise is added for robust learning

## Slide 23: Training and Clustering
Variational Autoencoder is used to learn the underlying relationship between path and orientation data.
RMS and KL-Divergence Losses are used during training
Multiple fully connected VAE architectures were tested.
Latent space signatures of the complete database are generated and clustered using K-Means Clustering.

## Slide 24: Inference example
Use the trained model and clustered database to generate a variety of mechanisms.

## Slide 25: Sample Problem

## Slide 26: Unified Motion Synthesis
Unified Design of Spatial, Spherical and Planar Mechanisms for the Motion Synthesis Problem

## Slide 27: Motion Synthesis Problem
Input- Spatial Poses
Output- Synthesized Mechanism

## Slide 28: Spatial, Spherical and Planar Mechanisms
Spatial 5-SS Mechanism
Planar RRRR Mechanism
Spherical RRRR Mechanism
Three Family of mechanisms for which motion synthesis algos exist.

## Slide 29: Motivation
A unified algorithm which can generate spatial, spherical or planar mechanisms doesn’t exist.
Unify spatial SS/PS dyad and RR dyad synthesis.
Express RR dyad as a sphere-plane or sphere-sphere intersection.

## Slide 30: Existing Spatial SS/PS dyad Solver
1. Kinematic Mapping based Geometric constraints
2. Bilinear constraints
3. Dyadic Parameters

## Slide 31: Existing Spatial SS/PS dyad Solver
1. Impose Geometric constraints
2. Impose Bilinear constraints

## Slide 32: Seven Poses on a Sphere/Plane
The approach is not able to generate solution dyads when spatial poses lie on a sphere or a plane.
There exist 3- SS/PS solutions
Bilinear constraints are rank-reduced

## Slide 33: Seven Poses on a Sphere/Plane
Calculate the characteristic-plane or –sphere using zero length coupler dyad i.e. c1,c2,c3=0
Singular vector denotes and FP coordinates can be calculated.
Four singular vectors of [Z] define the 4D null-space of . It can be back-substituted to find 3-dyad solution space.

## Slide 34: Five Poses on a Sphere/ Plane
First, we check if a characteristic-sphere or -plane exists. If not, only SS dyads exist.
There exist an additional 2- SS dyads whose intersection with characteristic sphere/plane constraint represent valid RR dyads.
1- spherical constraint isolated by imposing =1, finding and finding 2D nullspace of [W1]
Unique dyad calculated from 1- spherical constraints by random sampling.
FP and MP on characteristic primitive can be calculated

## Slide 35: Synthesis of spatial SS dyads

## Slide 36: Synthesis of spherical RR dyads

## Slide 37: Synthesis of planar RR dyads

## Slide 38: Planar Alt-Burmester Synthesis
A Motion Synthesis Approach to Solving Alt-Burmester Problems by Exploiting Fourier Descriptor Relationship Between Path and Orientation Data

## Slide 39: Planar Alt-Burmester Problem
Only Poses
Only Path Points
Poses + Path Points
Path Synthesis
Alt-Burmester Synthesis
Motion Synthesis

## Slide 40: Algorithm
Add missing orientations to path points and convert the problem into a pure motion synthesis problem
Carry out simultaneous Type and Dimensional synthesis using efficient motion synthesis algorithm

## Slide 41: Task curve computation
  : Task curve Fourier descriptors
  : Prescribed time information
  Point coordinates in complex form
  Frequency index
  Angular velocity of crank
  time interval over which task curve is defined
and are calculated by minimizing the fitting error
Task Curve equation:
Notes: A task curve is defined as a Fourier series as shown in the equation. It is characterized by its FDs Tk and the time interval tmax.
Tk and tmax are calculated by minimizing the fitting error function which represents the quality of fit of task curve to path points.
Once we have the task curve, we can move to the next step.

## Slide 42: Calculating unknown orientations
Coupler angle
Coupler point
Notes: To find the missing orientations, we need a relationship between the task curve FDs and coupler point orientation since they are dependent on each other for a four-bar mechanism. To develop this relationship, we first represent the Coupler angle as a Fourier series. The Coupler angle FDs are directly related to the Coupler point FD using the following relationships which can be derived using the vector sum equation.

## Slide 43: Calculating unknown orientations
Coupler orientation
Closed-form Fourier relationship between orientations and path descriptors
Notes: The coupler orientation is the sum of fixed link angle, coupler ang and the angle at which moving frame is fixed. This equation can be used to relate the Coupler angle FDs to coupler orientation FDs. Now, an explicit relationship can be found out by eliminating the coupler angle FDs from the path and orientation equations and simplifying it algebraically. The equation is dependent on three constants z1,z2 and z3 which are called Mixed synthesis parameters or MSP.

## Slide 44: Calculating unknown orientations
System of equation between orientation and path FDs
Known -Pose orientations are used to calculate MSP.
When , least square solution to MSP
When , unique solution to MSP
Notes: The relationship can be written as a system of equation to find the unknown MSPs using known pose orientations. >,=,< 3 poses lead to different cases.

## Slide 45: Calculating unknown orientations
When , the system of equations is under-constrained.
Additional constraints are called mixed constraints (MIC) which are
  Specify coupler parameters i.e.
  Specify actuating fixed pivot i.e.
  Specify scale of input link, orientation of fixed pivot line, and initial angle i.e.
Calculated MSP are used to generate missing orientations.
Notes: Once we have calculated the MSPs based on specified orientation and task path, we can generate the missing orientations using the same relationship. This results in an m+n pose problem.

## Slide 46: Algebraic fitting based motion synthesis
Map poses to quaternion space
Calculate coefficients of G-manifold coefficient matrix
Notes: Since the problem is now of Motion synthesis, we use algebraic fitting based algorithm. It enables simultaneous type and dimensional synthesis and efficient computation.
The G-manifold can represent dyadic constraints for dyads involving both R or P joints.

## Slide 47: Algebraic fitting based motion synthesis
System of equation solved using SVD.
Additional C-manifold constraint equations.
When , additional motion constraints (MOC) are required which are
  Fixed pivot location using line or point constraints.
  Moving pivot location using line or point constraints.
Type and dimensional synthesis of up to six unique four-bar mechanism.
Notes: is the G-manifold coefficient matrix. is the column vector of homogenous coefficients.
Finally, we can generate the four- bar mechanism. Let us combine all the pieces and see how the algorithm deals with generalized m-pose n-path mixed synthesis problem.
[𝐴] is the G-manifold coefficient matrix. 𝒒 is the column vector of homogenous coefficients.
Finally, we can generate the four- bar mechanism. Let us combine all the pieces and see how the algorithm deals with generalized m-pose n-path mixed synthesis problem.

## Slide 48: Unified m-pose n-path synthesis algorithm
MIC- Mixed constraint
MOC- Motion constraint
FD- Fully defined
X- Trivial/ under defined

## Slide 49: Example 1: Reverse Engineering a Mechanism
Five pose, seven path-points
Notes: The average path error measured by calculating the deviation of input points from final path using the Euclidean distance is 0.0694 units for the displayed configuration. The maximum angular deviation among all the given poses is for the pose 3 as 0.0736 rad.(4 degree)

## Slide 50: Example 2: Mixed synthesis with fully-constrained MSP computation
Three pose, five path-points mixed synthesis
Eight pose motion synthesis
Notes: Average path error is 0.0226 units while the maximum angular deviation for poses is 0.0106 rad (.6 degree) for second pose.

## Slide 51: Example 3:Under-constrained mixed synthesis
Two pose, four path-points mixed synthesis using additional mixed constraint
Three pose, one path-points mixed synthesis using additional motion constraint

## Slide 52: Planar Path Synthesis
An Optimal Parametrization Scheme for Path Generation Using Fourier Descriptors for Four-Bar Mechanism Synthesis

## Slide 53: Path Synthesis Problem
Existing algorithm for path synthesis is efficient but works in limited conditions.
The proposed improvements enhances the quality of results found by the path synthesis algorithm.

## Slide 54: Effect of assuming uniform time parametrization
Good result with proposed algorithm
Poor result with existing algorithm

## Slide 55: Path Synthesis using FD: Review
Task curve
4D minimization problem
Objective function
Mechanism parameters
  : Task curve Fourier descriptors
  : Prescribed time information
  Point coordinates in complex form
  Frequency index
  Angular velocity of crank
  time interval over which
  task curve is defined
Relationship with Path FD

## Slide 56: Family of parametrizations
Uniform time parametrization considers only task curves which have uniform speed which drastically reduce the possible task curves.
Non-uniform parametrization used to generate richer space of task curves.
A family of chord-length based time parameterizations have been proposed where is defined as
  : time parameter associated with the path point
  : coordinates of path point
  : parametrization control variable

## Slide 57: Optimal Parametrization
Cost of selected parametrization
The two dimensional search space is
: Total cost
: Fitting cost
: Harmonic cost
: Speed cost
Notes: A cost metric is proposed to estimate the quality of a parametrization. It has three distinct parts. Minimizing the cost function yields optimal alpha and tmax to be used.

## Slide 58: Optimal Parametrization: Fitting cost
Normalized fitting cost for a task curve
Notes: First cost term represents normalized fitting cost for the task curve. P2 Norm of the error for each path-point divided by number of points. Ensures accurate task curve.

## Slide 59: Optimal Parametrization: Harmonic cost
Harmonic analysis of four-bar coupler curves have the magnitude of higher order harmonics to be negligible.
Normalized weighted harmonic magnitude for a task curve
Notes: Second cost term represents harmonic cost. Past studies on Harmonic content of four-bar have shown that the magnitude of higher order harmonic is negledgible. To find task curves which follow this inherent four-bar coupler curve property, a cost function is designed. It penalizes large magnitudes on higher order harmonics.

## Slide 60: Optimal Parametrization: Speed cost
Speed of coupler point is
Speed cost can be defined using quadratic penalty function as
  : Maximum to minimum task curve speed ratio
  : Minimum speed ratio bound specified by user
  : Maximum speed ratio bound specified by user
Notes: Large coupler speed changes can lead to large induced forces on the links. This could compromise their rigidity and render the kinematic analysis useless.
In contrast, a uniform speed motion of the coupler can also be undesirable in instances like a quick-return mechanism.
Thus, enforcing a speed based criteria over the task curve gives users more control in design.
We use Speed ratio based penalty function to enforce the speed criteria.

## Slide 61: Example
<2
=0.3509, =0.0228
=0.0591, =0.0067
=0.1813, =0.0444
Task curve speed

## Slide 62: Unified Simulation
Using a Point-Line-Plane Representation for Unified Simulation of Planar and Spherical Mechanisms.

## Slide 63: Simulation
Visualization capability of a design tool is dependent on its simulation solver.
GIM
PMKS
SAM
Linkage
VEMECS
Synthetica
No unified planar and spherical n-bar kinematic simulators

## Slide 64: Issues with Commercial Packages
For detail design
Slower than purely kinematic simulators
Creation of feature-based assembly and initializing constraints on these systems is a nontrivial task.
Changing the type of joints or the number of links for a mechanism is also more complex.

## Slide 65: Planar and Spherical geometric constraints
Planar mechanism constraints
Spherical mechanism constraints

## Slide 66: Iterative solver
Simulation Algorithm
System of constraint equations
q: State vector
[J(q)]: Jacobian matrix
(q): Residual vector
Newton-Rhapson iteration

## Slide 67: Examples
Spherical Watt I six-bar mechanism
Watt's steam engine mechanism

## Slide 68: Examples
Spatial 5-SS platform linkage
Planar Stephenson II six-bar linkage
Spherical RRPR four-bar linkage

## Slide 69: Summary

## Slide 70: Dissertation Contributions
Alt-Burmester Synthesis
- ML approach for spatial mechanisms
- Analytical approach for planar mechanisms
Motion Synthesis
- Analytical approach for unified synthesis of planar, spherical, and spatial mechanisms
Path Synthesis
- ML approach for spatial mechanisms
- Analytical approach for planar mechanisms
Kinematic Analysis
- Numerical approach to simulate planar, spherical and spatial mechanisms

## Slide 71: Thank You